## Slide 1
Model Checking
Simulation
Implementation
UPPAAL Model
Stateflow
Chart
C Code
implementation
UPP2SF
Model Translation
Simulink Coder
Pacemaker
Heart
Non-deterministic
Deterministic
FPGA
implementation
Interpolation
HDL Coder
Notes: On the pacemaker side, we developed a model based design tool chain for pacemaker. The closed-loop system including the pacemaker and the heart are first modeled in model checker UPPAAL and some safety properties are checked.
Using the tool UPP2SF, which is a matlab script developed by us, the UPPAAL model of the pacemaker can be rigorously translated into stateflow chart
Using the realtime workshop in simulink, the stateflow chart can be translated into C code and implemented on any embedded platform.
Using this automated tool chain, we can rule out discrepancies introduced by manual translations between layers. Together with our heart model implementation, we can ensure all properties satisfied at verification level still holds after implementation.